## Slide 1: Visionscape .NET Training – Build Your Own App in Less Than 1 hour
Steven King

## Slide 2: Visionscape .NET Controls - Custom User Interfaces, Fully Integrated Vision
Notes: What the product is. Why is it significant. How to sell it.

## Slide 3: Visionscape .NET Controls - Benefits of Vision .NET Capability
Custom User Interfaces
  Simple
  Application Specific
  Automatic Job Creation
  Password Access Levels
Integrate Vision Directly with Automation
  One UI to control entire machine
  Tightly coupled Vision Results
  Interactive Calibration
  Access to all Microsoft .NET Capability
    Data Base
    Comm
    Etc.
C:\Microscan\Vscape\Documentation\ Visionscape .NET Programmer’s Manual.pdf
Notes: What the product is. Why is it significant. How to sell it.

## Slide 4: Visionscape .NET Training – Topics
Interactively build a Load and Run Example
  Load .AVP from Disk
  Download .AVP to the camera
  Run Mode
    Get Reports from Camera. Data Display
    Get Images from Camera. Image Display
    Virtual Triggering
  Setup Mode
    Setup Manager View – Adjust and Test Job
    Step Tree View – Manipulate Job in Step Tree View
  Extra Features
Monitoring Multiple Cameras in Run Mode
Notes: What the product is. Why is it significant. How to sell it.

## Slide 5: Visionscape .NET Training – Main Runtime Controls for Load and Run
PC
JobStep
  File Open
  File Save
  File New
AVP
Vision System Step
Inspection
Snapshot
Blob Tool
Formatted Output
VsCoordinator – Finds and Allocates Control for all Vs Devices
VsDevice
  Take Control
  Download Job
  Start
  Stop
ReportConnection
  Retrieve Image
  Retrieve Results
IOConnection
  Triggering
Notes: What the product is. Why is it significant. How to sell it.

## Slide 6: Visionscape .NET – Key Components for Handling Devices
VsCoordinator – AVP Backplane
  Finds all vision devices on PC or on Network
  Makes them available for use by single user
  “Device Discovery”
VsDevice – Control The Vision Device (Emulator, GigE, Smart Camera)
  Take Control
  Download
  Start
  Stop
Notes: What the product is. Why is it significant. How to sell it.

## Slide 7: Visionscape .NET – Key Components Job Creation and Control
JobStep – File Manager
  Allows you to open, save and create new AVP files
Step – Job Manipulation
  Allows you to create Jobs programmatically
  Add Steps programmatically
  Get and Set Resource Datums (Parameters, ROI position, etc.)
  Assign Results for Upload
Notes: What the product is. Why is it significant. How to sell it.

## Slide 8: Visionscape .NET – Key Components for Run Mode
ReportConnection
  Get Results from an Inspection on Device
BufferView
  Display Images During Runtime
  Multiple Buffer Views Allowed
ReportView, StatsView, ResultsView
  Display Auto Formatted Results
  ReportView combines Stats and Results
IO Connection
  Get and Set IO on device
  Trigger via Virtual IO
Notes: What the product is. Why is it significant. How to sell it.

## Slide 9: Visionscape .NET – Key Components for Setup Mode
Setup Manager
  Job Editing
  Job Tryout
  Set RootStep to Inspection to connection
  Set RootStep to Null to disconnect
Step Tree Editor
  Job Tree Editing
  Set RootStep to Inspection to connection
  Set RootStep to Null to disconnect
Notes: What the product is. Why is it significant. How to sell it.

## Slide 10: Visionscape .NET Example – Create New Visual Studio Project
Launch Visual Studio 2010 (or Visual C# 2010 Express).
From the File Menu, choose “New Project…” (or “New Project…” from the Start Page.)
In the New Project dialog, choose “Visual C#” as your language, and then choose “Windows Forms Application” as your project template type.
Set to .Net Framework 4
Enter “CSharpExample” for the “Name”
Choose the “Location” for where you want to store your project
Press OK.
Notes: What the product is. Why is it significant. How to sell it.

## Slide 11: Visionscape .NET Example – Add References to Project
Go to the Project menu
Select “Add Reference”
Select “Browse” tab
Navigate to “C:\Microscan\Vscape\Assembly”
Select and Add References to the following Visionscape assemblies:
  Visionscape.dll
  Visionscape.Communications.dll
  Visionscape.Devices.dll
  Visionscape.Steps.dll
Click OK
Notes: What the product is. Why is it significant. How to sell it.

## Slide 12: Visionscape .NET Example – Add “Display” Components to Project
Using Explorer, Navigate to “C:\Microscan\Vscape\Assembly”
Select the following :
  Visionscape.Display.Devices.dll
  Visionscape.Display.Reporting.dll
  Visionscape.Display.Image.dll
  Visionscape.Display.Setup.dll
Drag these to the General Tab in the Toolbox
You now have all the components we will use in this example
Notes: What the product is. Why is it significant. How to sell it.

## Slide 13: Visionscape .NET Example – Change Embed Interop Type
Under References
Select Visionscape
Change “Embed Interop Type” from True to False
This will change “Copy Local” from False to True. If not, do it explicitly.
Do the same thing for “stdole”
Notes: What the product is. Why is it significant. How to sell it.

## Slide 14: Visionscape .NET Example – Set Up Your Form
Make Form Bigger
Drag a “BufferView” onto form
Drag a “SetupManager” onto form
Add buttons for:
  Run Mode
  Trigger
  Setup Mode
  Load AVP
  Create AVP
Add textBox1 and textBox2
Rename buttons appropriately, i.e.
  btnRunMode, btnTrigger …
Notes: What the product is. Why is it significant. How to sell it.

## Slide 15: Visionscape .NET Example – Add Form Load and Form Closing Events
Click on the Main Form
Select Events in Properties
Double Click on Load
Double Click on FormClosing
You should now have this code
Notes: What the product is. Why is it significant. How to sell it.

## Slide 16: Visionscape .NET Example – Add “Using” for key references
Add the following snippet to the top of the form
using Visionscape;
using Visionscape.Steps;
using Visionscape.Devices;
using Visionscape.Communications;
Notes: What the product is. Why is it significant. How to sell it.

## Slide 17: Visionscape .NET Example – Add key member variables
Add the following snippet to the partial class of the Form
private VsCoordinator m_Coord; // For starting avp backplane
private JobStep m_Job; // For opening and saving jobs
private VsDevice m_Dev; // For controlling the vision device
private ReportConnection m_RepCon1; // For getting report and image from camera
private InspectionReport report; // Contains report coming back from camera
private IOConnection m_IO; // IO connection to the device for physical and virtual IO
private VisionSystemStep vs; // Visionsystem Step for job handling
private string DEVICENAME; // Global to hold name of device
Notes: What the product is. Why is it significant. How to sell it.

## Slide 18: Visionscape .NET Example – Instantiate these objects (new)
Add the following snippet to Form_Load
// Show Buffer View, Hide Setup Manager
bufferView1.Show();
setupManager1.Hide();
// Instantiate all of our global objects
m_Coord = new VsCoordinator(); // Starts Backplane
m_Job = new JobStep();
m_RepCon1 = new ReportConnection();
m_IO = new IOConnection();
// Set DEVICENAME to your units name
DEVICENAME = "SoftSys1";
//DEVICENAME = "MicroHAWK187700";
Notes: What the product is. Why is it significant. How to sell it.

## Slide 19: Visionscape .NET Example – Set up event to discover device (camera)
Add the following snippet to Form_Load. This will connect to the device once it is found by m_Coord.
Hit TAB, TAB to complete the line
Finally add this line to have Coordinator alert the program when the device has been discovered.
You will see the following event code added
// Set up and event heandler to be called when AVP Backplane discovers my device
m_Coord.OnDeviceFocus +=
// Tell coordinator to fire the OnDeviceFocus event when the my DEVICENAME is discovered
m_Coord.DeviceFocusSetOnDiscovery(DEVICENAME, -1);
Notes: What the product is. Why is it significant. How to sell it.

## Slide 20: Visionscape .NET Example – Populate OnDeviceFocus Event Function
Optional if you want to see IO transitions from the camera.
Type in first part of line, +=, and the Tab Tab to autocomplete the line, and add the events.
void m_Coord_OnDeviceFocus(VsDevice objDevice)
{
// Get handle to the Device
m_Dev = objDevice;
// Connect the IO control to the device. Only do this once.
m_IO.Connect(m_Dev);
// Create an event so that we see when IO on camera changes
// m_IO.IOTransition += new EventHandler<IOConnectionEventArgs>(m_IO_IOTransition);
// Initialize all IO to low, in this case Virtual 1
m_IO.PointWrite(VsIoType.Virtual, 0, false);
// Load our job from disk
m_Job.Load("C:\\Microscan\\Vscape\\Jobs\\test.avp");
// Get the first VisionSystemStep in the job
vs = m_Job.VisionSystemStep();
// Connect the VisionSystemStep to our device
vs.SelectSystem(m_Dev.Name);
//Now we can download to the device(vision system) and run the job on that device
m_Dev.Download(vs, true);
// Connect reports to the inspection on the device
m_RepCon1.Connect(DEVICENAME, 1, ReportConnection.ConnectOptions.DEFAULT);
// Make images part of the report
m_RepCon1.AddSnapBuffers((Visionscape.Steps.InspectionStep)m_Job.FindBySymName("Insp1"));
// Now start the device
m_Dev.StartAll();
}
Notes: What the product is. Why is it significant. How to sell it.

## Slide 21: Visionscape .NET Example – Set up event to get reports
Add the following snippet to Form_Load. This will create a Report Event that gets called when a new report is uploaded.
FormLoad now looks like this
// Create event handler for when report gets sent from device to the pc
m_RepCon1.NewReport +=
Notes: What the product is. Why is it significant. How to sell it.

## Slide 22: Visionscape .NET Controls – Create a Test Job
Simple Blob Job
Count Dark Parts
Ignore Blobs That Touch ROI
Set for Results Upload
  Inspection Status
  Number of Blobs
Save Job
  “c:\vscape\jobs\test.avp”
Notes: What the product is. Why is it significant. How to sell it.

## Slide 23: Visionscape .NET Example – Populate NewReport Event Function
void m_RepCon1_NewReport(object sender, ReportConnectionEventArgs e)
{
// Get the Inspection report
report = e.Report;
// Get Number of Blobs
bool status;
long numBlobs;
status = report.Results[0].AsBool;
textBox1.Text = status.ToString();
numBlobs = report.Results[1].AsInt;
textBox2.Text = numBlobs.ToString();
//does our report contain any images, if so display it?
if (report.Images.Count > 0)
{
//extract the image as a BufferDm,
//and set it into the Buffer View
bufferView1.Buffer = (BufferDm)report.Images[0];
}
// This is a good place to collect unused memory
GC.Collect();
}
This gets the first and second result datums. Types must be matched.
Set image into BufferView if image count > 0
Always, always include this line or you can get memory drain
Notes: What the product is. Why is it significant. How to sell it.

## Slide 24: Visionscape .NET Example – Unwind all controls during shutdown
private void Form1_FormClosing(object sender, FormClosingEventArgs e)
{
// Stop all inspections
if (m_Dev != null)
m_Dev.StopAll();
// Disconnect the reports
if (m_RepCon1 != null)
m_RepCon1.Disconnect();
m_RepCon1 = null;
// Disconnect the IO
if (m_IO != null)
m_IO.Disconnect();
m_IO = null;
// Disconnect from the camera
if (m_Dev != null)
m_Dev.Disconnect();
m_Dev = null;
// Set the RootStep of setup manager to null
setupManager1.RootStep = null;
// Clear the job from pc memory
while (m_Job.Count > 0)
m_Job.Remove(1);
m_Job = null;
}
Notes: What the product is. Why is it significant. How to sell it.

## Slide 25: Visionscape .NET Example – Run the example
Job will load and run
It will show images and data
Buttons not functional yet
Stop by closing form
Notes: What the product is. Why is it significant. How to sell it.

## Slide 26: Visionscape .NET Example – Run Mode Button
private void btnRunMode_Click(object sender, EventArgs e)
{
// Show Buffer View
bufferView1.Show();
// Hide Setup Manager
setupManager1.Hide();
setupManager1.RootStep = null;
// Download Job to Device
m_Dev.Download(m_Job, true);
// Connect reports to the inspection on the device
m_RepCon1.Connect(DEVICENAME, 1, ReportConnection.ConnectOptions.DEFAULT);
// Make images part of the report
m_RepCon1.AddSnapBuffers((Visionscape.Steps.InspectionStep)m_Job.FindBySymName("Insp1"));
// Now start the device
m_Dev.StartAll();
}
Notes: What the product is. Why is it significant. How to sell it.

## Slide 27: Visionscape .NET Example – Setup Mode Button
private void btnSetupMode_Click(object sender, EventArgs e)
{
// Stop the device and disconnect reports
m_Dev.StopAll();
m_RepCon1.Disconnect();
// Show setupManager1 starting with Inspection as first step
setupManager1.ListViewSize = 80;
setupManager1.ImageViewSize = 300;
setupManager1.ZoomAuto();
setupManager1.RootStep = (Visionscape.Steps.Step)m_Job.FindBySymName("Insp1");
setupManager1.Show();
// Hide Run View
bufferView1.Hide();
}
Choose what is displayed as part of these controls
Example : setupManager1.OptionLayoutSet(Visionscape.Display.Setup.SetupManagerLayoutOptions.ShowToolbar,false);
Turns off Toolbar so you can create your own buttons for Acquire, Live, Tryout etc.
Notes: What the product is. Why is it significant. How to sell it.

## Slide 28: Visionscape .NET Example – Trigger Button
private void btnTrigger_Click(object sender, EventArgs e)
{
// Set IO to low, in this case Virtual 1
m_IO.PointWrite(VsIoType.Virtual, 0, false);
// Put in short delay
System.Threading.Thread.Sleep(5);
//Set IO to high, in this case Virtual 1
m_IO.PointWrite(VsIoType.Virtual, 0, true);
}
Go To Setup Mode
Change Trigger Virtual 1
Go To Run Mode
Tryout Trigger
Notes: What the product is. Why is it significant. How to sell it.

## Slide 29: Visionscape .NET Example – Extra Credit – Add Report View
ReportView
  Add ReportView to Form
  Hook in NewReport
// Get the Inspection report
report = e.Report;
// Dump results to report view
reportView1.Report = report;
Notes: What the product is. Why is it significant. How to sell it.

## Slide 30: Visionscape .NET Example – Extra Credit – Open AVP From File
Open AVP from File
  See btnLoadAVP_Click
Notes: What the product is. Why is it significant. How to sell it.

## Slide 31: Visionscape .NET Example – Extra Credit – Auto Create an AVP
Programmatically Create AVP
  See btnCreateAVP_Click
  Use StepBrowser
    Input Datums
    Resource Datums
    Output Datums
Notes: What the product is. Why is it significant. How to sell it.

## Slide 32: Multiview Display Example
Example using Device Dropdown
Notes: What the product is. Why is it significant. How to sell it.

## Slide 33: Microscan Advanced Programming Capabilities
Visionscape .NET Programming
  Requires Visionscape to be loaded onto the PC
Rest APIs/Serial Command Set
  Visionscape does not need to be installed
WEB SDK
  For MicroHAWK ID - http://www.microscan.com/en-us/support/download-center
Notes: What the product is. Why is it significant. How to sell it.

## Slide 34: Wrap Up
A follow up email will be sent to you. Please respond with comments or questions.
  sking@microscan.com
  visionsupport@microscan.com
A link to the presentation and example programs will be in the email.
Thank you very much, and Good Programming!
Notes: What the product is. Why is it significant. How to sell it.

## Slide 35: Visionscape .NET Training – Build Your Own App in Less Than 1 hour
Steven King
Sking@microscan.com